## Slide 1
Wireless Security
Keamanan Komputer dan Jaringan VER 2019

## Slide 2
What have made wireless networks so popular?

## Slide 3: Wireless

## Slide 4: Wireless LAN Architecture
Infrastructure Mode
Ad-hoc Mode
IEEE 802.11 base
  Institute of Electrical and Electronic Engineers (IEEE) has issued number of protocols.
Wireless Fidelity (Wi – Fi)
  WiFI Alliance : promoting WLAN.

## Slide 5: A Hybrid wireless and Ethernet network

## Slide 6: Drawback of Wi-Fi
    Radio frequency interference
  Using radio wave to transmit the signal.
  Signal interference issues
Security flaw
  Easy to eavesdrop
  Poor Authentication
  Rouge Access Point
  DoS attack

## Slide 7: Wardriving
Wardriving is the act of driving around with equipment that can be used to detect Wi-Fi access points located in homes and businesses.

## Slide 8: Strong signal jamming
In this simple and direct DoS attack, an attacker uses a wireless transmitter to broadcast interference on the same frequency channel used by the access point, effectively drowning it out and creating so much radio frequency (RF) noise that Wi-Fi devices in the area can’t operate

## Slide 9: Security Protection
  Access Control
    Implements Media Access Control (MAC) address filtering.
  Wired Equivalent Privacy (WEP)
    Wireless encryption.
    RC4 algorithm.
  Authentication
    To ensure all the legitimate user enable to use or access the sources/services.
    Type of authentication :
      open system base : Service Set Identifier (SSID).
      shared key authentication : WEP.

## Slide 10: MAC Filtering
How it works
  Access permission is given based on MAC address listed.
Security Flaw
  MAC address is spoofed easily.
  Man – in – the – middle attack (MIMA)

## Slide 11: MAC Spoofing

## Slide 12: MAC Spoofing

## Slide 13: WEP
  The goals:
    Authentication
    Confidentiality
    Integrity
  Use shared key and random 24-bit string initialization vector (IV).
Two levels encryption:
  64 bits key : 40-bit encryption and 24-bit IV (Initial Vector)
  128 bits : 104-bit encryption and 24-bit IV

## Slide 14: How WEP work (1)

## Slide 15: How WEP work (2)

## Slide 16: WEP Authentication (1)
Access
Point
Station
Authentication Request
Authentication Challenge
Authentication Response
Authentication Result
Notes: 1. An authentication request management frame is sent requesting use of “shared key” authentication
2. The responder sends an authentication management frame containing 128 octets of challenge text to the initiator (this text is in the clear – plaintext) generated using the WEP pseudo-random number generator with the “shared secret” and a random initialization vector (IV). The IV is always sent in the clear.
3. The initiator encrypts the challenge with the shared key and the IV and sends to responder.
4. The responder verifies the 32-bit CRC integrity check value (ICV) and verifies that the challenge matches. Success/fail status is returned to the initiator

## Slide 17: WEP Authentication (2)
1. The client station transmits an authorization request.
2. The access point returns a challenge string in the clear.
3. The client chooses an IV.
4. Using the IV and secret base key, the client encrypts the challenge string.
5. The client station sends the IV and encrypted challenge string to the access point.
6. The access point also encrypts the challenge string using the transmitted IV and the same secret base key.
7. If the client’s encrypted challenge string is identical to the challenge string sent by the client station, the association occurs.

## Slide 18: Security Flaw
IV is too small and transmitted in clearttext form.
IV static.
WEP combines IV with key.
WEP does not provide protection to integrity.
  Non-cryptographic Cyclic Redundancy Check (CRC) to check the integrity a packet and acknowledge it with correct checksum.

## Slide 19: SSID
Device identity.
Security Flaw
  Not support encryption.
  Rouge Access Point attack.
  Spoofing attack.

## Slide 20: Rogue Access Point
a rogue access point is an access point set up by a cracker to collect data such as passwords, usernames, or credit card numbers.

## Slide 21: WPA
Using Temporal Key Integrity Protocol (TKIP) as solution to the encryption problem in WEP.
  Dynamic key
  Adding the size of IV
  Michael (message integrity check) to prevent message modification.
Using Extensible Authentication Protocol (EAP) to authenticate including digital certificate, username & password, smart card, and another.

## Slide 22: DoS attack

## Slide 23: 802.11i
802.11i Architecture consist of :
  IEEE 802.1x for authenticating.
    Using EAP and server authentikasi
  Robust Secure Network provide high security level to secure user and network communication.
    IEEE 802.1X to access control.
  AES (Advanced Encryption Standard)-based CCMP (Counter Mode/CBC – MAC Protocol) to provide confidentiality, integrity, and authetication.

## Slide 24: The comparison of WEP, WPA, and IEEE 802.11i

## Slide 25
END