## Slide 1: Circuit components
Active vs. Passive components
  Active ones may generate electrical power.
  Passive ones may store but not generate power.
Lumped vs. Distributed Constants
  Distributed constant components account for propagation times through the circuit branches.
  Lumped constant components ignore these propagation times. Appropriate for circuits small relative to signal wavelengths.
Linear, time invariant (LTI) components are those with constant component values.

## Slide 2: Active circuit components
Conservation of energy: active components must get their power from somewhere!
From non-electrical sources
  Batteries (chemical)
  Dynamos (mechanical)
  Transducers in general (light, sound, etc.)
From other electrical sources
  Power supplies
  Power transformers
  Amplifiers

## Slide 3: Passive lumped constants
Classical LTI
  Resistors are AC/DC components.
  Inductors are AC components (DC short circuit).
  Capacitors are AC components (DC open circuit).
Other components
  Rectifier diodes.
  Three or more terminal devices, e.g. transistors.
  Transformers.